## Slide 1
Structural option for the Jinping neutrino central detector
Contributor： Yuanqing Wang, Zongyi Wang
Speaker： Zongyi Wang
Department of civil engineering, Tsinghua University
2015-06-05
1

## Slide 2
Outline
Introduction of the whole structure
Bearing capacity of the local joint
Introduction of the 1 t scale model
2

## Slide 3
Two alternative options:
(1) Cylindrical scheme
(2) Spherical scheme
The structure is placed at 2400 m underground. 500 t (2) or 1000 t detecting liquid (density 0.8-1 g/cm3) is contained by an acrylic vessel and water with the density of 1.0 g/cm3 is outside the acrylic.
The acrylic vessel is supported by a stainless steel latticed shell.
Project introduction
Introduction of the whole structure
3

## Slide 4
Include PMT
No PMT
Cylindrical scheme (study in progress)
Diameter of acrylic vessel 11 m，height 11 m
Diameter of latticed shell 16 m，height 16 m
Fiducial capacity of the vessel 572 t
Introduction of the whole structure
4

## Slide 5
Spherical scheme (study in progress)
Diameter of acrylic ball 12 m
Diameter of latticed shell 17 m
Fiducial capacity of the vessel 523 t
Introduction of the whole structure
Include PMT
No PMT
5

## Slide 6
Acrylic vessel + double-layer stainless steel
At 700 m underground
Diameter of ball 35.5 m，thickness 120 mm
Diameter of stainless steel：inner 38.5 m，outer 40.5 m.
20 thousands of liquid scintillator (0.866g/cm3) inside, water outside (1g/cm3). 15,000 PMT mounted on the latticed shell.
Working condition:
Structural self weight + self weight and buoyancy of PMT + pressure difference on the acrylic ball
Design experience for JUNO central detector
6

## Slide 7
The point on the inner latticed shell
The point on the outer latticed shell
Number of the braces: 564
Lighting-blocking rate: 1.8%
Dividing method
Along the latitude line：24
Along the longitude line：15
7
Design experience for JUNO central detector

## Slide 8
The numerical model was created and evaluated using the ABAQUS
Maximum stress on the ball: 5.4 MPa
Singular points excluded: 3.9 MPa
Maximum stress on the latticed shell: 82.7 MPa
Maximum axial force of braces: 134.6 KN
Maximum displacement of structure: 24.5 mm
1/1428
Strength analysis
8
Design experience for JUNO central detector

## Slide 9
Stability analysis
Load factor 2.12 > 2.0
Eigenvalue of the 1st buckling mode 4.3 > 4.2
Material nonlinearity + geometric nonlinearity，
the initial imperfection is taken as 1/300 of the span.
“Technical specification for space frame structures”
9
Design experience for JUNO central detector

## Slide 10
Schematic diagram
Joint 1
Joint 2
Joint 3
Bearing capacity of the local joint
Test purpose:
Bearing capacity
Deformation ability
Failure mode
Load in JUNO: 14 t
100 t tensile jack
10

## Slide 11
The width of the connecting area: 250 mm.
The reacting force was provided by four ground anchors.
Fixing device
Fixing device
11

## Slide 12
Joints 1 and 2
Loads on Joints 1 and 2 were sideling--angle 5°.
Loading device
Joint 3
To study the ultimate bearing capacity
Load was vertically upward
Installing error
12

## Slide 13
Comparison between test and FE results under 14 t
design load（14 t）
number | Comparative item | Measure point | Test result | FE result
Joint 1 | Stress (MPa) | A1-1 | 4.722 | 5.534
 |  | B5-1 | 3.954 | 1.476
 |  | C10-1 | 2.647 | 1.713
 | Displacement(mm) | W1-1 | 0.814 | 0.985
Joint 2 | Stress (MPa) | A8-2 | 2.525 | 2.909
 |  | B7-2 | 2.593 | 1.703
 |  | C13-2 | 2.461 | 2.580
 | Displacement(mm) | W2-2 | 0.625 | 1.032
Joint 3 | Stress (MPa) | A7-3 | 8.467 | 8.392
 |  | B7-3 | 3.479 | 2.963
 |  | C1-3 | 3.262 | 3.093
 | Displacement(mm) | W4-3 | 0.512 | 0.630
8.5 MPa, on the patched acrylic
3.4 MPa, on the main acrylic
Limit within 10 MPa
14
Yield strength of acrylic: 50 MPa

## Slide 14
Joint 1
Ultimate bearing capacity 288 KN, 2 times the design value
Failure picture
Joint 2
Ultimate bearing capacity 325 KN, 2.3 times the design value
Joint 3
Ultimate bearing capacity 513 KN, 3.6 times the design value
13

## Slide 15
Displacement values in these three joint tests are all very small (less than 2 mm).
  The test results of Joint 3 accord with FE results better. It shows that Joint 3 is less affected by initial defects and its stress distribution is more uniform.
  The ultimate strength of Joints 1, 2 and 3 are 28.8 t, 32.5 t and 51.3 t, respectively.
  The maximum axial force of braces of the Jinping central detector will be less than 14 t on account of its smaller scale. This kind of joint is reliable.
Conclusion
15

## Slide 16
Black film
Support to fix PMT
Include tank
No tank
Diameter of acrylic ball 1.2 m
Diameter of stainless steel tank 2 m, height 2 m
Length of PMT 300 mm
Introduction of the 1 t scale model
Daya Bay
16

## Slide 17
Thanks!