## Slide 1: Design Requirements for Jinping Underground Neutrino Experiment
2015.06.05
Guanghua Gong
Dept. of engineering Physics, Tsinghua University
Neutrino experiment

## Slide 2: Outline
Physics requirements
Detector concept
LS/Water/WbLS
Purification system
PMT
Electronics/Trigger/DAQ
Prototypes

## Slide 3: Physics requirements
Fiducial mass
  >1Kt
Energy range:
  0.1MeV – 100MeV
Energy resolution:
  500 – 1000 PE/MeV
Directionality:
  20°for E> 5MeV
Particle identification
  Cherenkov and scintillation separation
  Gamma vs. electron vs. alpha-proton-nuclear-recoil
Calibration
  Energy response nonlinearity <1%
  Position reconstruction bias <1cm (@r=6m)

## Slide 4: Detector(s) arrangement
130m tunnel
Option1: dual detectors
Option2: single detector
Depends on civil situation

## Slide 5: Target Mass: Sphere or Cylinder
Cylinder
Sphere

## Slide 6: Detector concept
cylinder sphere

## Slide 7: Major detector components
SS framework
Acrylic vessel
PMT
Black shield
Veto PMT
Water buffer
SS vessel
Tyvek reflector
Target material
Water buffer
From inner to outer

## Slide 8: Target material
Assumptions
  PMT QE : 20% (35% for HQE PMT)
  Coverage: 50% ~ 80%
To reach 500~1000 PE/MeV resolution, light yield of target material
2000~10000 photons/MeV
Notes: HQE with high dark rate

## Slide 9: Target material : Water/LS/WbLS
Target range
  Minfang Yeh

## Slide 10: More information from WbLS
Cherenkov light must dominate in the 1st 10 ns over scintillation light
Scintillation requirement
  Light yield
  Ʈ > 100ns (if S=C in 10ns)
fast Cherenkov light
Slow scintillation light
Cherenkov lights provide direction info. for charge particles.
  non-solar background suppression
  Electron/Photon separation

## Slide 11: PMT requirements
Dimension: 8” / 9” / 20”
QE: >20%
TTS: <5ns
  Related to the S/C separation
  Longer Ʈ of WbLS will relax the requirement
FWHM: <10ns
Low radioactivity background
Coverage: 50% ~ 80%
  2500(20”) ~ 15000(8”)

## Slide 12: Calibration
Energy response non-linearity : <1%
  Position reconstruction bias: <1cm (@r=6m)
  (6.02/6)**3 -1 = 1%
Optical and radiation sources
Rope loop for 4-π deployment

## Slide 13: Electronics/trigger/DAQ/DCS
FADC with 1Gsps/12b readout of each PMT
  Patten recognition, C/S separation
  information reconstruction, better event quality
Trigger-less scheme
  Self-trigger for each PMT, event selection by CPU
  PMT Dark noise and long scintillation lifetime
  Challenges for DAQ
Electronics under water
  Better signal quality
  Engineering challenges
    seal, cable/connectors, reliability

## Slide 14: Prototype(s)
20L
1t
20t
Cosmic with Telescope
Topic: WbLS Light yield
See Mohan’s talk
30PMT + WbLS
Topic:
α/β/γ separation,
Direction recon,
particle identification
Relocate able in container
200PMT + WbLS
Topic:
radioactivity background
PMT study,
Material purification
Engineering verification
2014
2015
2016

## Slide 15: Other topics
Purification
  Water / scintillator / nitrogen
Calibration
PMT protection
Magnetic shielding?
thermal environment / temp. control
Low radioactivity materials
Infrastructure
and many…..

## Slide 16: Summary
CJPL-II provides great opportunity for low-background neutrino experiment.
Feasible conceptual detector design, detail scenario depends on civil situation
Major experimental requirements settled down
Prototypes testing are under going
Many aspects are not started ….

## Slide 17: Thank you!